## Slide 1: Binary Primer
Number systems

## Slide 2: Number systems
Decimal: 10 symbols (0,1,2,3,4,5,6,7,8,9)
Binary: 2 symbols (0,1)
Odometer system for counting
  Each digit is a dial with every symbol
  Advancing past last symbol resets to first
    Digit to the left advances by one.

## Slide 3
Decimal (10 symbols)
00
01
02
03
04
05
06
07
08
09
10
11
12
13
14
15

## Slide 4
Decimal (10 symbols) Binary (2 symbols – 4 bit representations)
00 0000
01 0001
02 0010
03 0011
04 0100
05 0101
06 0110
07 0111
08 1000
09 1001
10 1010
11 1011
12 1100
13 1101
14 1110
15 1111

## Slide 5: Binary to Decimal (sum of products)
place: 1000’s 100’s 10’s 1’s
8439 = (8 * 103) + (4 * 102) + (3 * 101) + (9 * 100) = 8000 + 400 + 30 + 9
= 8439

## Slide 6: Binary to Decimal (sum of products)
place: 1000’s 100’s 10’s 1’s
8439 = (8 * 103) + (4 * 102) + (3 * 101) + (9 * 100) = 8000 + 400 + 30 + 9
= 8439
place: 8’s 4’s 2’s 1’s
11012 = (1 * 23) + (1 * 22) + (0 * 21) + (1 * 20)
= 8 + 4 + 0 + 1
= 13

## Slide 7: Decimal to Binary: div 2 into quotient, store remainders in a stack
Translate 87 into Binary:
43, R 1
2 87
8710 = 12

## Slide 8: Decimal to Binary: div 2 into quotient, store remainders in a stack
Translate 87 into Binary:
43, R 1 21, R 1
2 87 2 43
8710 = 112

## Slide 9: Decimal to Binary: div 2 into quotient, store remainders in a stack
Translate 87 into Binary:
43, R 1 21, R 1 10, R 1
2 87 2 43 2 21
8710 = 1112

## Slide 10: Decimal to Binary: div 2 into quotient, store remainders in a stack
Translate 87 into Binary:
43, R 1 21, R 1 10, R 1 5, R 0
2 87 2 43 2 21 2 10
8710 = 01112

## Slide 11: Decimal to Binary: div 2 into quotient, store remainders in a stack
Translate 87 into Binary:
43, R 1 21, R 1 10, R 1 5, R 0
2 87 2 43 2 21 2 10
2, R1
2 5
8710 = 101112

## Slide 12: Decimal to Binary: div 2 into quotient, store remainders in a stack
Translate 87 into Binary:
43, R 1 21, R 1 10, R 1 5, R 0
2 87 2 43 2 21 2 10
2, R1 1, R 0
2 5 2 2
8710 = 0101112

## Slide 13: Decimal to Binary: div 2 into quotient, store remainders in a stack
Translate 87 into Binary:
43, R 1 21, R 1 10, R 1 5, R 0
2 87 2 43 2 21 2 10
2, R1 1, R 0 0, R1 (MSD)
2 5 2 2 2 1
8710 = 10101112

## Slide 14: Reverse check accuracy
10101112 =
(1 * 26) + (0 * 25) + (1 * 24) + (0 * 23) +
(1 * 22) + (1 * 21) + (1 * 20)
= 64 + 0 +16 + 0 + 4 + 2 + 1 = 8710

## Slide 15: Reverse check accuracy
10101112 =
(1 * 26) + (0 * 25) + (1 * 24) + (0 * 23) +
(1 * 22) + (1 * 21) + (1 * 20)
= 64 + 0 +16 + 0 + 4 + 2 + 1 = 8710
Place: 64 32 16 8 4 2 1
1 0 1 0 1 1 12 = 64 + 16 + 4 + 2 + 1 = 87

## Slide 16: Hexadecimal
16 symbols (0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F)
A16 => 1010
B16 => 1110
C16 => 1210
D16 => 1310
E16 => 1410
F16 => 1510 So what is 1016?

## Slide 17
Decimal (10 symbols) Hex (16 symbols) Binary (2 symbols)
00 00 0000
01 01 0001
02 02 0010
03 03 0011
04 04 0100
05 05 0101
06 06 0110
07 07 0111
08 08 1000
09 09 1001
10 0A 1010
11 0B 1011
12 0C 1100
13 0D 1101
14 0E 1110
15 0F 1111
16 10 10000